## Slide 1
Kid Camera
Waveshare ESP32-S3-Touch-LCD-2
เอกสารอธิบาย Architecture · Flow · Source Code
MCU
ESP32-S3-WROOM-1 240 MHz dual-core Xtensa LX7
Flash / RAM
8 MB QIO Flash + 8 MB OPI PSRAM
Display
ST7789T3 2.0" IPS 240×320 SPI @ 80 MHz
Camera
OV2640 HQVGA preview / SVGA capture (JPEG)
Storage
MicroSD card (shared SPI bus with display)
Frameworks
PlatformIO · Arduino · GFX 1.4.0 · JPEGDEC 1.8
Page 1 / 8

## Slide 2
Hardware Architecture
Slide 2 / 8
ESP32-S3 240 MHz · 320 KB SRAM 8 MB Flash · 8 MB PSRAM
ST7789T3 Display
240×320 IPS SPI 80 MHz
OV2640 Camera
CSI · HQVGA/SVGA JPEG mode
CST816D Touch
I²C 0x15 GPIO 47/48/46
MicroSD Card
SPI shared bus SD_CS = GPIO41
Buzzer (Passive Piezo)
PWM tone() GPIO 18
USB-C CDC Serial
USB OTG (native) 115200 baud
SPI Bus (SCK=39, MOSI=38, MISO=40)
I²C Bus (SDA=48, SCL=47)
CSI (Parallel) XCLK,PCLK,VSYNC HREF,Y2-Y9

## Slide 3
Software Modules (Source Files)
Slide 3 / 8
config.h
Pin Definitions & Constants
GPIO map, UI colors, WiFi creds, photo path, app constants
display.h/.cpp
GFX Display Driver
Arduino_GFX ST7789 @ 80 MHz SPI Backlight control, fillScreen
touch.h/.cpp
CST816D Touch Driver
I²C Wire, read XY coords, debounce in main.cpp
cam.h/.cpp
OV2640 Camera Driver
esp_camera_init(), HQVGA preview SVGA capture, frame grab/return
sdcard.h/.cpp
SD Card File I/O
SD.begin(SD_CS), save/list/delete JPEG files in /photos/
buzzer.h/.cpp
Buzzer Sound
tone(GPIO18) shutter click two-note 80 ms sequence
wifi_server .h/.cpp
AsyncWebServer AP Gallery
WiFi SoftAP, AsyncWebServer HTTP gallery + photo + delete APIs
main.cpp
State Machine & Orchestration
setup(), loop(), 4 states: VIEWFINDER/CAPTURE/GALLERY/PHOTO_VIEW
← config.h ถูก #include โดยทุก module
main.cpp เป็นตัว orchestrate ทุก module ผ่าน function calls

## Slide 4
Module Call Map — ใครเรียกใคร
Slide 4 / 8
main.cpp (setup + loop)
display_init() gfx→ draw*()
touch_init() touch_read()
cam_init() cam_get_preview() cam_capture()
sdcard_init() sdcard_save_photo() sdcard_list_photos() sdcard_delete_photo()
buzzer_init() buzzer_shutter()
wifi_server_start() wifi_server_stop() wifi_get_ip()
_jpeg.openRAM() _jpeg.decode() draw_jpeg_from_sd()
JPEGDEC lib
JPEGDEC lib
→ callback → gfx→draw16bitRGBBitmap()

## Slide 5
State Machine Flow Chart
Slide 5 / 8
BOOT (setup)
display_init() → ST7789 SPI init + backlight on
touch_init() → CST816D I²C probe
cam_init() → OV2640 JPEG HQVGA mode
sdcard_init() → SD.begin(), scan /photos/
buzzer_init() → pinMode LOW
Splash screen → orange background 600 ms
STATE_VIEWFINDER (default)
loop(): cam_get_preview() → JPEGDEC decode → gfx draw draw_info_bar() · draw_ctrl_bar() · debounced_touch()
tap SHOOT
tap PICS
tap WiFi → wifi_server_start/stop()
STATE_CAPTURE
do_capture(): fillScreen white cam_capture() SVGA sdcard_save_photo() buzzer_shutter()
→ back
STATE_GALLERY
draw_gallery(): 6 thumbs/page sdcard_list_photos() draw_jpeg_from_sd(JPEG_SCALE_EIGHTH) ← tap thumb → PHOTO_VIEW
← back

## Slide 6
Camera & JPEG Pipeline
Slide 6 / 8
▶ LIVE PREVIEW (every loop frame)
OV2640 HQVGA 240×176
JPEG buffer (PSRAM)
JPEGDEC openRAM() decode(0,0,0)
gfx→ draw16bit RGBBitmap()
ST7789 Display y=0..175
▶ PHOTO CAPTURE (tap SHOOT)
OV2640 SVGA 800×600
JPEG buffer ~100 KB
SD.open() FILE_WRITE write(buf)
/photos/ IMGxxxx .jpg
buzzer shutter() tone()
▶ GALLERY THUMBNAIL (draw_gallery)
SD card /photos/ IMGxxxx.jpg
ps_malloc() read to PSRAM buf
JPEGDEC openRAM() decode(x,y,8)
74×74 px thumbnail on screen
drawRect border gray
JPEG_SCALE_EIGHTH = 8 → 800×600 ÷ 8 = 100×75 px (ใส่ใน slot 74×74 ได้พอดี)

## Slide 7
WiFi Gallery + SPI Bus Sharing
Slide 7 / 8
WiFi Access Point Gallery
• SSID: "KidCamera" Password: "12345678" IP: 192.168.4.1
• tap [WiFi] button → wifi_server_start() → AsyncWebServer.begin()
• GET / → buildPage() อ่าน /photos/* จาก SD แล้วสร้าง HTML
• GET /photo?file=IMG0001.jpg → req→send(SD, path, image/jpeg)
• DELETE /delete?file=IMG0001.jpg → SD.remove(path)
• safe_filename() ป้องกัน path traversal (../ และ \)
• Browsers เปิดได้จาก phone/PC บน WiFi เดียวกัน
SPI Bus Sharing (Display + SD)
SCK = GPIO 39 MOSI = GPIO 38 MISO = GPIO 40
LCD_CS = GPIO 45 → Arduino_GFX ควบคุม
SD_CS = GPIO 41 → SD library ควบคุม
✓ CS แตกต่างกัน → ใช้ bus ร่วมกันได้ไม่ conflict
✓ display_init() ต้องเรียกก่อน sdcard_init()
(GFX เริ่ม SPI bus, SD ใช้ bus ที่เริ่มแล้ว)
✓ 80 MHz สำหรับ Display / 40 MHz สำหรับ SD
หน้าจอ Portrait 240×320
Camera Preview y = 0 .. 175 (240×176 px HQVGA)
Info Bar y = 176 .. 199 (photo count, WiFi IP)
Control Bar y = 200 .. 319 [PICS] [●SHOOT] [WiFi]
Control Bar Buttons
PICS x:4-74 y:CTRL_Y +10..+110
SHOOT r=46 px center (120,260)
WiFi ON=Green OFF=Gray x:166-236

## Slide 8
วิธีต่อยอด & ปรับแต่ง
Slide 8 / 8
🎨 เปลี่ยนสี UI
config.h → แก้ COLOR_* constants ตัวอย่าง: #define COLOR_BG 0x18E3 (navy)
📷 เปลี่ยนความละเอียดกล้อง
cam.cpp → cfg.frame_size = FRAMESIZE_XGA (1024×768) cam.cpp → cfg.jpeg_quality = 8 (คุณภาพสูงขึ้น)
🔊 เปลี่ยนเสียง Shutter
buzzer.cpp → แก้ tone(BUZZER_PIN, 4000, 25) เพิ่ม / ลด frequency และ duration
🌐 เพิ่ม Station Mode WiFi
wifi_server.cpp → WiFi.begin(ssid, pass) แทน softAP แก้ WIFI_AP_SSID/PASS ใน config.h
🖼 เพิ่ม State ใหม่
main.cpp → เพิ่ม enum AppState { ..., STATE_SETTINGS } เขียน draw_settings() + handle_settings_touch()
⚡ ประหยัดไฟ
main.cpp → esp_sleep_enable_timer_wakeup() display_backlight(false) เมื่อไม่ touch 30 วิ
ไฟล์หลักที่ต้องแก้ส่วนใหญ่: config.h (pins/constants) · main.cpp (logic) · cam.cpp (camera settings)